Scheduler Manual
D. Rabinowitz 2025 Oct 27

1. Overview

   The LS4 scheduler code reads in a plan of observations (aka “fields”) from a text file, and sends commands to the control programs for the telescope (questctl) and the LS4 camera (ls4_ccp ) to implement the observations. The scheduler determines which fields will be observed and their order depending on codes in the observing plan and observational constraints specific to the type of observation.

2. Observation Plan

Each line of an observation plan ("obsplan") specifies the following:
ra, dec : telescope pointing (hours, deg)
expt : exposure time in sec
shutter code : ( explained below)
n_required : required number of exposures
interval : requested exposure interval (sec)
survey code (explained below).
comment (extra reference info)

Survey Codes (integer from 0 to 4):
0: no survey
1: Trans-Neptunian Object survey
2: Supernova survey
3: Must-do high-priority code
4: Ligo event followup

Shutter Codes (upper or lower case N,Y,F,P,E,M, or L):
N: dark field (see note below)
Y: sky field
F: focus field
P: pointing-calibration field
E: evening twilight flag
M: morning twilight flat
L: dome flat
Note: darks with dec = -1, 0, 1 deg will be observed in evening twilight, dark time, and morning twilight, respectively. Otherwise, there is no time restriction.

3. Observation Selection

Before each observation, the scheduler updates the status of every planned observation. The relative status of the observations and their selection constraints determine the next observation to make.

Selection Constraints

- pointing limits (e.g. limiting airmass, hour angle, galactic latitude, moon separation)
- exposure requirements (expt, n_required, interval)
- observable sky (visible area of night sky).
- interruptions (dome closed for weather or maintenance).
- observation cadence (minimum time between observations).
- survey code (survey-specific constraints)

Field Descriptor

Every field has a descriptor with pertinent status and observing parameters (see "Field" structure in "scheduler.h"):

- survey code (from obsplan)
- shutter code (from obsplan)
- status code ( “too late”, “not doable”, “ready”, “do_now” )
- pointing info (ra, dec, galactic lat, long, lunar separation)
- observation info ( expt, n_required, interval, shutter code)
- rise/set info (UT hours and Julian Days ut_rise, ut_set, jd_rise, jd_set)
- expected time of next exposure (Julian Date jd_next).
- number of completed exposures (n_done)
- up time before field sets or sun rises (time_up)
- completion time for remaining observations (time_required)
- time left before time_required exceeds time_up (time_left)
- exposure info for completed exposures (filename, ut, jd, lst, ha, am, expt)
- doable flag set to 1/0 if field is/isn’t observable any time during the night

Selection Algorithm

init_fields (start of night):

Initialize field descriptors for every observation.
Set n_observable to number of doable fields.

get_next_field (each time a new observation is made):

Loop through the field descriptors for each observation. Determine the field indices of the earliest fields in the obsplan meeting the following criteria:

Field Index Criterion
i_min_do_now sky fields with do-now status
i_min_dark dark fields with do-now status
i_min_flat dome or sky flat
Also keep tallies of fields meeting the following criteria:

Tally Criterion
n_ready_must_do ready status, must-do survey code
n_late_must_do too-late status, must-do survey code
n_ready ready status, not must-do survey code
n_do_now do-now status, all survey codes
n_late too-late status

Also find the minimum values for the following quantities for fields meeting the specific criteria

Minimum Value Quantity Criterion
n_left_min_must_do number of exposures remaining ready status, must-do
n_left_min number of exposures remaining ready status, not must-do
n_do_now do-now status
n_late too-late status

for each observation:
   update_field_status (determine if doable and set status code)

Cadences

  The cadence of the observations depends on the staging of 4 key
  operations:

(1) exposure time (time shutter is open).
(2) image readout time (~20 sec for dual-amp readout, ~40 sec for
   single-amp readout).
(3) transfer time of the image data from the controllers to the
   host computer (~5 sec).
(4) the time to slew and position the telescope and dome for the
   next observation (> 20 sec).

  candence 1. linear staging
The simplest way to stage the operations is one at a time.

cadence 1: expose -> readout -> transfer -> slew -> ....

  cadence 2. Parallel slew

A faster cadence is achieved by parallel staging the telescope slew
  during the image readout and transfer:

expose -> readout -> transfer -> exposure -> readout -> transfer -> ...
   slew slew

  cadence 3. Parallel slew and transfer

    The optimal cadence is achieved by parallel staging slew and transfer
  with readout and expose. This is possible because the camera controllers
  have multiple buffers in memory allowing transfer of previously read
  image data while new data are being read out:

expose -> readout -> expose -> readout -> expose -> readout -> ...
   slew transfer slew transfer slew

  Currently, only cadence 1 is implemented.